## Slide 1: Bandwidth efficient object recognition for drone swarms
School of Computer Science and Communication Systems
Master in Computer Science
Supervised by
Prof. Dario Floreano
Dr. Giuseppe Cocco
Fabian Schilling
Student
Marco Zoveralli
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476

## Slide 2: Project Overview
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
1/13
Motivation
  Detection Accuracy: prediction by single drone may be unreliable
  Consensus: autonomous swarms may need to agree on whether a given target is present
  Bandwidth efficiency: especially relevant in urban environment
Goal
                Determine the presence/absence of a target object with high accuracy
Proposed approach
                Exploit multiple viewpoints
                Estimations are done locally by each drone
                Final vote sent to a base station
                Limited information exchange to save power, bandwidth and for scalability
What? – Related Work – How? – Validation – Conclusion
Notes: When considering a set of devices performing object recognition, a swarm of drones in our case, what can happen is that some drone cannot predict the presence or absence of the object in a too reliable way. This is where a distributed solution comes into help: the devices that are part of the swarm put together the single predictions in order to get a more reliable one. One of the main requirements when considering such approaches, besides improving the accuracy of the predictions, is to save bandwidth.

## Slide 3: Project Overview
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
1/16
Motivation
  Detection Accuracy: prediction by single drone may be unreliable
    False positives and false negatives can occur
  Consensus: autonomous swarms may need to agree on whether a given target is present
  Bandwidth efficiency: especially relevant in urban environment
Goal
                Determine the presence/absence of a target object with high accuracy
Introduction – Related Work – How? – Experiments – Conclusion
Notes: When considering a set of devices performing object recognition, a swarm of drones in our case, what can happen is that some drone cannot predict the presence or absence of the object in a too reliable way. This is where a distributed solution comes into help: the devices that are part of the swarm put together the single predictions in order to get a more reliable one. One of the main requirements when considering such approaches, besides improving the accuracy of the predictions, is to save bandwidth.

## Slide 4: Related Work
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
2/16
J. Lee et al., “Real-Time Object Detection for Unmanned Aerial Vehicles based on Cloud-based Convolutional Neural Networks”, First IEEE International Conference on Robotic Computing (IRC), 2017.
  Cloud-based object detection
  Applied to aerial vehicles, but no data aggregation
A. Giusti et al., "Cooperative sensing and recognition by a swarm of mobile robots“, IEEE/RSJ International Conference on Intelligent Robots and Systems, 2012.
                Interesting communication and consensus
                Human-computer interaction
                Different setup, different goal
                Classification task
A. Rahimpour et al., “Distributed Object Recognition in Smart Camera Networks”, 2016 IEEE Int. Conf. on Image Processing (ICIP), 2016.
  Feature extraction performed by each camera
  Features sent to a base station, which performs
  object detection  no autonomy of devices
  Lack of an autonomous set of devices that
  triggers other events
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Different assumption for giusti’s paper: they assume that while the protocol is running, the object is indeed there. Instead, we have to determine whether an object is there: there might be nothing as well.

## Slide 5
Simple Network Management Protocol
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
3/13
Hardware Selection and Validation
What? – Related Work – How? – Validation – Conclusion
Hardware selection
  Project inputs
    Single-board computers: Odroid XU4
    Image Acquisition: M7 camera
  Our proposal
    Connectivity: WiFi Module 5
Hardware validation
  Connectivity tests
    Adhoc mode compatibility
    Network throughput
    Network stability
  Object detection tests
    Setup of a machine learning framework on the ARMv7 architecture
    MSCOCO pre-trained neural network
    Average computational time: 200ms per prediction
    Accurate predictions over a defined set of objects (e.g. bottle, keyboard)
Notes: What does model checking do? A little background.

## Slide 6
Simple Network Management Protocol
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
3/16
Hardware Selection and Validation
Hardware selection
  Single-board computers: Odroid XU4
  Image Acquisition: OpenMV M7
  Connectivity: WiFi Module 5
Connectivity tests
  Adhoc mode compatibility
  Network throughput
  Network stability
Object detection tests
  Setup of a deep learning framework
  MSCOCO pre-trained neural network
Introduction – Related Work – How? – Experiments – Conclusion
Notes: What does model checking do? A little background.

## Slide 7: Protocol Design: Inter-host Communication
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
4/16
Intra-host
Inter-host
  Aggregate local predictions with received ones
  Weighted average over the set of predictions
  Emission of final result
Challenges
  Give the proper weight to each device’s prediction
  Reach a consensus
  Handle packet losses
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Infer about BIP, say that we discuss later about the tools

## Slide 8: Protocol Design: Intra-host Computations
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
5/16
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Infer about BIP, say that we discuss later about the tools

## Slide 9: Protocol Design: Leader Election
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
6/16
Assumption: the number of hosts (N) in the network is known
Any host can be the leader
  As long it knows who the leader is
One leader per round
  It changes at each round
  More system resiliency
  Very simple mechanism
Leader ID = Round ID % N
  N = #hosts
The leader classifies an object as present iff #positive predictions > M
  M = N/K
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Infer about BIP, say that we discuss later about the tools

## Slide 10: Protocol Design: Exchanged Messages
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
7/13
Probe
Status
Final Prediction
Acknowledgement
Start Round
Limited amount of exchanged messages
  N-1 probes messages  1 single broadcast
  N-1 status messages
  1 final vote
  N-1 start round messages  1 single broadcast
What? – Related Work – How? – Validation – Conclusion
Notes: Infer about BIP, say that we discuss later about the tools

## Slide 11: Protocol: Execution Example
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
7/16
Limited amount of exchanged messages
  N-1 probes messages  1 single broadcast
  N-1 status messages
  1 final vote + ACK
  N-1 start round messages  1 single broadcast
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Infer about BIP, say that we discuss later about the tools

## Slide 12: Protocol: Execution Example
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
8/13
What? – Related Work – How? – Validation – Conclusion
Notes: Infer about BIP, say that we discuss later about the tools

## Slide 13: Protocol Validation: Data Fusion
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
8/16
Precision: TP / (TP+FP)
  High if there are few false positives
Recall: TP / (TP + FN)
  High if there are few false negatives
Two scenarios
With the real object
  Not all optimal views
With the fake object
  Some views resemble the real object
Simulation
  Take K pictures
  Fix N
  For each possible combination of N hosts in K positions (for a total of Ck,n), compute the prediction with the data fusion mechanism
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Our model is good at detecting people  we will try to detect a person
… data fusion mechanism, meaning that the system will detect the object as present iff #positive votes > M

## Slide 14: Protocol Validation: Data Fusion, P(loss) = 0
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
9/16
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Our model is good at detecting people  we will try to detect a person

## Slide 15: Protocol Validation: Data Fusion, P(loss) = 10%
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
10/16
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Our model is good at detecting people  we will try to detect a person

## Slide 16: Protocol Validation: Data Fusion, P(loss) = 20%
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
11/16
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Our model is good at detecting people  we will try to detect a person

## Slide 17: Protocol Validation: Data Fusion, P(loss) = 30%
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
12/16
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Our model is good at detecting people  we will try to detect a person

## Slide 18: Protocol Validation: Data Fusion, P(loss) = 40%
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
13/16
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Our model is good at detecting people  we will try to detect a person

## Slide 19: Protocol Validation: Data Fusion, P(loss) = 50%
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
14/16
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Our model is good at detecting people  we will try to detect a person

## Slide 20: Protocol Validation: Protocol Convergence
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
15/16
Simple setup
  Three devices
  Same object as data aggregation validation
Two distinct runs
With the real object
  False negatives eliminated
With the fake object
  False positives eliminated
Introduction – Related Work – How? – Experiments – Conclusion
Notes: Infer about BIP, say that we discuss later about the tools

## Slide 21: Conclusion
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
16/16
Distributed object detection system implemented
  Implemented from scratch
  Scalable and modular system
  Improvements over single-host system have been shown
  Main goal achieved
Future Work
  Gather more data
  Re-train the model
  Deploy the protocol on more devices
  Perform tests on flying/moving drones
Introduction – Related Work – How? – Experiments – Conclusion
Notes: More data could have given stronger results
  Only 9 different views were considered for the data validation
More devices could have shown more usefulness
  Only 3 drones/Odroids were available

## Slide 22: Progress
1/11
École polytechnique fédérale de Lausanne – A.Y. 2018/2019 – Marco Zoveralli – Sciper N. 267476
7/7
What? – Related Work – How? – Progress
Notes: Infer about BIP, say that we discuss later about the tools

## Slide 24
Simple Network Management Protocol
École polytechnique fédérale de Lausanne – A.Y. 2016/2017 – Marco Zoveralli – Sciper N. 267476
7/26
Model Checking: Abstraction VS Refinement
Why? – What? – How? – Progress – Conclusion
Notes: What does model checking do? A little background.